Modifying STM NUCLEO432KC

### The pin in use :

The static pin configuration is defined in file RootDir/local/NUCLEO432/board.cfg
Important pins, are :
PA03    CASTEL_ICU2     ICU               AF:TIM15_CH2   #ARD_A2
PA05    CASTEL_ICU1     ICU               AF:TIM2_CH1    #ARD_A4
PA08    CASTEL_PWM1     PWM               AF:TIM1_CH1    #ARD_D9
PA11    CASTEL_PWM2     PWM               AF:TIM1_CH4    #ARD_D10
### principle :
For each ESC channel, there is two pins : PWM generation, and ICU input capture.
The two pins has to be linked, and the resulting wire has to be connected to a resistor pullup (2.2kΩ 1/4W resistor conencted to 3.3V)

### Wiring :

### Soldering :